## Slide 1: PEIC Final Project Project plan and topics
Group1: 邱于瑄、林均翰、劉展佑、張顥譽
Presenter:林均翰
Date:2026.05.21

## Slide 2: Outline
Literature review
Project spec.
Behavior model simulation

## Slide 3: Project
V2 Constant ON-Time control for point of load (POL) buck
Motivation
  Ultrafast Transient Response
  Simple Implementation (no current sensing resistor)
Spec & Application:
  Vin = 12V, Vo = 1.2V Io = 1A to 4A
  CPU or GPU in mobile device

## Slide 4: Spec.
Topology
Input voltage Vin
Output voltage Vo
Output current Io
Inductance L
Capacitor C
ESR
External ramp slope Se = 3Sf
Switching frequency fs
Output Voltage Ripple
Buck Converter
12 V
1.2 V
4 A
1.8 μH
800 uF
175 uΩ
350 mV/us
300 kHz
0.0012 V

## Slide 5: V2COT Small-Signal Control to Output Transfer Function
Gvc Control to Output Transfer Function
The ESR of ceramic capacitors and TON are small, it can be simplified to:

## Slide 6: V2COT Small-Signal Control to Output Transfer Function
Gvc Control to Output Transfer Function
Double complex poles

## Slide 7: V2COT Small-Signal Control to Output Transfer Function
Se > Se_K = 3Sf
Se = Sf < Se_K
Se > Se_K = 15Sf
Insufficient External Ramp
PM too low.
System instability.
Sufficient External Ramp
Sufficient PM.
System stability .
Excessive External Ramp
Bandwidth limitations.
Poor transient response

## Slide 8: Compensator Design
Type I
fsw =300 kHz , Set fc=0.1 fsw , fsw=30kHz
At low frequency (before 1/2 fsw), both Gain and Phase are 0.
Therefore, compensator can be achieved through an integrator.
The bandwidth design avoids phase margin insufficiency caused by double poles at 30kHz.

## Slide 9: Loop Gain Transfer Function
Crossover Frequency : 31kHz
Gain Margin : 17.1 dB
Phase Margin : 89.4 degree
Type 1 Compensator Circuit
Loop Gain

## Slide 10: Behavior Model Simulation @ Start-Up
Vout
IL
Vcom
Vramp

## Slide 11
Behavior Model Simulation @ Steady State

## Slide 12: Transient Response @ Step Down 4A → 1A
Duty
Io
Vout
IL
Vo , Vcom
Vramp
Overshoot = 1.5mV
Settling time = 20.38us
20.38us
1.5mV
(6Tsw )

## Slide 13: Transient Response @ Step Down 4A → 1A
Duty
Io
Vout
IL
Vo , Vcom
Vramp
18.43us
1.8mV
Overshoot = 1.8mV
Settling time = 18.43us
(5Tsw )

## Slide 14: To-do item
IC subblock design and simulation
Specifications for subblocks