## Slide 1: PEIC Final Project Project plan and topics
Group1: 邱于瑄、林均翰、劉展佑、張顥譽
Presenter: 邱于瑄
Date: 2026.05.28

## Slide 2: Outline
Literature review
Project spec.
IC subblock design and simulation
  Operation Amplifier
  Current Source
To-do item

## Slide 3: Project
V2 Constant ON-Time control for point of load (POL) buck
Motivation
  Ultrafast Transient Response
  Simple Implementation (no current sensing resistor)
Spec & Application:
  Vin = 12V, Vo = 1.2V Io = 1A to 4A
  CPU or GPU in mobile device

## Slide 4: Spec.
Topology | Buck Converter
Input voltage Vin | 12 V
Output voltage Vo | 1.2 V
Output current Io | 4 A
Inductance L | 1.8 μH
Capacitor C | 800 uF
ESR | 175 uΩ
External ramp slope Se = 3Sf | 350 mV/us
Switching frequency fs | 300 kHz
Output Voltage Ripple | 0.0012 V
Our Topology

## Slide 5: Transistor-level subblock
OPA
High Speed Comparator
Current Source
Process: N16ADFP

## Slide 6: OPA – Schematic
Two-Stage Miller-Compensated OPA

## Slide 7: OPA – AC Analysis
Gain-Bandwidth: 10 MHz
Phase Margin: 76.43∘
Open-Loop Gain: 46.97 dB (223 V/V)

## Slide 8: Current Source – Schematic
Resistorless auto bias reference circuit
  Better Component Matching
  Save Space
  Low Power
  No Resistor Error
H.J. Oguey, D. Aebicsher, CMOS Current Reference without Resistance, IEEE J. Solid-State Circuits, Volume 32, pag. 1132-1135. 1977.

## Slide 9: Current Source – Simulation Result

## Slide 10: OPA & Current Source Integration
Crossover Frequency : 30.5 kHz
Gain Margin : 10.1 dB
Phase Margin : 89.2 degree
Dashed line: Ideal model Solid line: Transistor level
Crossover Frequency : 31 kHz
Gain Margin : 17.1 dB
Phase Margin : 89.4 degree

## Slide 11: To-do item
IC subblock design and simulation
  High Speed Comparator
MOS level blocks + behavior model blocks Simulation

## Slide 12: Reference
H.J. Oguey, D. Aebicsher, CMOS Current Reference without Resistance, IEEE J. Solid-State Circuits, Volume 32, pag. 1132-1135. 1977.