## Slide 1: PEIC Final Project Project plan and topics
Group1: 邱于瑄、林均翰、劉展佑、張顥譽
Presenter:邱于瑄
Date: 2026.06.04

## Slide 2: Outline
Literature review
Project spec.
IC subblock design and simulation
  Operation Amplifier (folded cascoded)
  High-Speed Comparator
To-do item

## Slide 3: Project
V2 Constant ON-Time control for point of load (POL) buck
Motivation
  Ultrafast Transient Response
  Simple Implementation (no current sensing resistor)
Spec & Application:
  Vin = 12V, Vo = 1.2V Io = 1A to 4A
  CPU or GPU in mobile device

## Slide 4: Spec.
Topology | Buck Converter
Input voltage Vin | 12 V
Output voltage Vo | 1.2 V
Output current Io | 4 A
Inductance L | 1.8 μH
Capacitor C | 800 uF
ESR | 175 uΩ
External ramp slope Se = 3Sf | 350 mV/us
Switching frequency fs | 300 kHz
Output Voltage Ripple | 0.0012 V
Our Topology

## Slide 5: Transistor-level subblock
OPA
High Speed Comparator
Current Source
Process: N16ADFP

## Slide 6: High Speed Comparator
Spec:
  Hysteresis: 5 mV - 20 mV, Propagation Delay: <1ns
  VDD = 1V, Iref = 60uA

## Slide 7: High Speed Comparator - Simulation Result
± 10mV
Propagation delay = 355ps
Propagation delay = 164ps

## Slide 8
Folded Cascode Opamp
Bias
First Stage
Second Stage
OPA

## Slide 9
Gain-Bandwidth: 86.28 MHz
Phase Margin: 101.4∘
Open-Loop Gain: 94.89 dB
CMRR = 101.4dB
OPA – AC analysis
Av = 94.89dB
101.4∘
CMRR = 101.4dB

## Slide 10
Compensator
Type I compensator
Gain-Bandwidth: 120.8 kHz
Phase Margin: 47.19∘

## Slide 11: Current Source – Schematic
Resistorless auto bias reference circuit
  Better Component Matching
  Save Space
  Low Power
  No Resistor Error
H.J. Oguey, D. Aebicsher, CMOS Current Reference without Resistance, IEEE J. Solid-State Circuits, Volume 32, pag. 1132-1135. 1977.

## Slide 12: Current Source – Simulation Result

## Slide 13: OPA & Current Source Integration
Crossover Frequency : 30.5 kHz
Gain Margin : 10.1 dB
Phase Margin : 89.2 degree
Dashed line: Ideal model Solid line: Transistor level
Crossover Frequency : 31 kHz
Gain Margin : 17.1 dB
Phase Margin : 89.4 degree

## Slide 14: To-do item
IC subblock design and simulation
MOS level blocks + behavior model blocks Simulation

## Slide 15: Reference
H.J. Oguey, D. Aebicsher, CMOS Current Reference without Resistance, IEEE J. Solid-State Circuits, Volume 32, pag. 1132-1135. 1977.