## Slide 1: PEIC Final Project Project plan and topics
Group1: 邱于瑄、林均翰、劉展佑、張顥譽
Presenter: 林均翰、劉展佑
Date: 2026.06.11

## Slide 2: Outline
Introduction
Project spec.
Behavior model simulation
IC subblock analysis and simulation
Conclusions
References

## Slide 3: Outline
Introduction
Project spec.
Behavior model simulation
IC subblock analysis and simulation
Conclusions
References

## Slide 4: Project Plan
V2 Constant ON-Time control for point of load (POL) buck
Motivation
  Ultrafast Transient Response
  Simple Implementation (no current sensing resistor)
Application
  Vin = 12V, Vo = 1.2V Io = 1A to 4A in
  CPU or GPU in mobile device

## Slide 5: Challenge of COT
Subharmonic Oscillation:
  Both the inductor current and the capacitor voltage ripple information is fed back to the modulator
  Delay due to the capacitor ripple results in sub-harmonic oscillation
  Subharmonic oscillation occurs when the ceramic capacitor is used, since the capacitor voltage ripple is relatively too large
Solution:
  Add external ramp to compensate the delay resulted from capacitor voltage ripple
  Advantage:
    Simple to implement
    No current sensing needed
Li, Jian, and Fred C. Lee. "Modeling of ${\rm V}^{2} $ Current-Mode Control." IEEE Transactions on Circuits and Systems I: Regular Papers 57.9 (2010): 2552-2563.

## Slide 6: Outline
Introduction
Project spec.
Behavior model simulation
IC subblock analysis and simulation
Conclusions
References

## Slide 7
Topology | Buck Converter
Input voltage Vin | 12 V
Output voltage Vo | 1.2 V
Output current Io | 4 A
Inductance L | 1.8 μH
Capacitor C | 800 uF
ESR | 175 uΩ
External ramp slope Se = 3Sf | 350 mV/us
Switching frequency fs | 300 kHz
Output voltage ripple | 0.0012V
Our Topology
Project spec
Outline

## Slide 8: Outline
Introduction
Project spec.
Behavior model simulation
IC subblock analysis and simulation
Conclusions
References

## Slide 9: System Architecture
Power Stage
Filter
VIN
VOUT
Type-I Compensation
Sensing Feedback
Vout
Ramp Generator
Summer
Comparator
Timing Generator
RS Latch
Logic Control
Compensation & Modulator

## Slide 10: Behavior model simulation (SIMPLIS)
Power Stage
Compensater
External Ramp
COT Generator
Comparator

## Slide 11: V2COT Small-Signal Control to Output Transfer Function
Gvc Control to Output Transfer Function
The ESR of ceramic capacitors and TON are small, and can be simplified to:
Double complex poles
Se: the slope of the external ramp during off-time
Sf = RCoVo / Ls

## Slide 12: Gvc under different ramp slope
Se > Se_K = 3Sf
Se = Sf < Se_K
Insufficient External Ramp
PM too low
System instability
Sufficient External Ramp
Sufficient PM
System stability
Se > Se_K = 15Sf
Excessive External Ramp
Bandwidth limitations
Poor transient response

## Slide 13: Gvc under different ramp slope
Se > Se_K = 3Sf
Se = Sf < Se_K
Insufficient External Ramp
PM too low
System instability
Sufficient External Ramp
Sufficient PM
System stability
Se > Se_K = 15Sf
Excessive External Ramp
Bandwidth limitations
Poor transient response

## Slide 14: Compensator Design
Type I
fsw =300 kHz , Set fc=0.1 fsw , fsw=30kHz
At low frequency (before 1/2 fsw), both Gain and Phase are 0.
Therefore, compensator can be achieved through an integrator.
The bandwidth design avoids phase margin insufficiency caused by double poles at 30kHz.

## Slide 15: Loop Gain Transfer Function
Crossover Frequency : 31kHz
Gain Margin : 17.1 dB
Phase Margin : 89.4 degree
Type 1 Compensator Circuit
Loop Gain

## Slide 16: Behavior Model Simulation
Vout
IL
Vcom
Vramp
@ Startup
@ Steady State
Vramp
Vcom
IL
Vout

## Slide 17: Behavior Model Simulation – Load transient (4A1A)
Duty
Io
Vout
IL
Vo , Vcom
Vramp
Overshoot = 1.5mV
Settling time = 20.38us
20.38us
1.5mV
(6Tsw )

## Slide 18: Behavior Model Simulation – Load transient (1A4A)
Duty
Io
Vout
IL
Vo , Vcom
Vramp
18.43us
1.8mV
Overshoot = 1.8mV
Settling time = 18.43us
(5Tsw )

## Slide 19: Outline
Introduction
Project spec.
Behavior model simulation
IC subblock analysis and simulation
Conclusions
References

## Slide 20: Transistor-level subblock
OPA
High Speed Comparator
Current Source
Process: N16ADFP

## Slide 21: High Speed Comparator
Spec:
  Hysteresis: 5 mV - 20 mV, Propagation Delay: <1ns
  VDD = 1V, Iref = 60uA

## Slide 22: High Speed Comparator - Simulation Result
± 10mV
Propagation delay = 355ps
Propagation delay = 164ps

## Slide 23
Folded Cascode Opamp
Bias
First Stage
Second Stage
OPA

## Slide 24
Gain-Bandwidth: 86.28 MHz
Phase Margin: 101.4∘
Open-Loop Gain: 94.89 dB
CMRR = 101.4dB
OPA – AC analysis
Av = 94.89dB
101.4∘
CMRR = 101.4dB

## Slide 25
Compensator
Type I compensator
Gain-Bandwidth: 120.8 kHz
Phase Margin: 47.19∘

## Slide 26
Current Source – Schematic
Resistorless auto bias reference circuit
  Better Component Matching
  Save Space
  Low Power
  No Resistor Error
H.J. Oguey, D. Aebicsher, CMOS Current Reference without Resistance, IEEE J. Solid-State Circuits, Volume 32, pag. 1132-1135. 1977.

## Slide 27
Current Source – Simulation Result

## Slide 28: Transistor Level Block in SIMPLS Simulation
4A - 1A
1A - 4A
Step-down load transient: peak at 1.210V, settling time = 0.04ms
Step-up load transient: peak at 1.197V, settling time = 0.1ms

## Slide 29: Outline
Introduction
Project spec.
Behavior model simulation
IC subblock analysis and simulation
Conclusions
References

## Slide 30: Conclusion
Successfully designed and verified the critical analog sub-blocks for a V2 Constant ON-Time controlled Buck converter at the transistor level using TSMC 16nm FinFET technology.
Successful Transistor-Level Design and Verification of Key Sub-Blocks:
  Folded Cascode OPA: Achieved a high open-loop gain of 94.89 dB and phase margin of 101.4°.
  Type I Compensator: Confirmed stable loop response with a Gain-Bandwidth Product of 120.8 kHz.
  Resistorless Current Sources: Successfully generated reference currents of 300.1 μA without utilizing physical resistors.

## Slide 31: Reference
Li, Jian, and Fred C. Lee. "Modeling of ${\rm V}^{2} $ Current-Mode Control." IEEE Transactions on Circuits and Systems I: Regular Papers 57.9 (2010): 2552-2563.
H.J. Oguey, D. Aebicsher, CMOS Current Reference without Resistance, IEEE J. Solid-State Circuits, Volume 32, pag. 1132-1135. 1977.